## Slide 1
10µM
ETH= 5.00 kV Mag= 2.40 KX WD= 9.4 mm Signal A= SE2
Presenter: Negar Ziehm
25 June 2026

## Slide 2: Table of content
08 | Q&A
01 | Introduction
02 | Litreture Review
03 | Dataset Characteristics
04 | Model
05 | Model development and evaluation
06 | Results, Challenges and Errors
07 | Discussion
1
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 3: Introduction
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm
2
Micro-Electro-Mechanical Systems
miniaturized devices integrated mechanical structures, sensors, actuators, and electronics
MEMS
Built on a single chip.
widely used in Sensors, biomedical devices communication systems and industrial applications
Scanning Electron Microscopy
uses a focused beam of electrons to scan a sample surface
SEM
Provides high-resolution images of micro/nano structures.
Essential for inspection and evaluating MEMS structures.

## Slide 4: Literature Review
3
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm
Key Results
Achieved ~90% classification accuracy
More confusion appeared for visually similar classes such as Patterned_surface and MEMS_devices_and_electrodes
Demonstrated that pretrained CNNs can successfully recognize complex SEM morphologies.
In the model comparison, Inception-v4 and Inception-ResNet-v2/“ResNet” gave comparable results, but the “ResNet” result was slightly worse and less stable at 5000 steps.
Methodology
Manually annotated 18,577 SEM images into 10 categories.
Used transfer learning / feature extraction with CNNs pretrained on ImageNet. Main model: Inception-v3.
For Inception-v3, they retrained mainly the last layers: softmax + fully connected layer.
Dataset split: 80% training, 10% validation, 10% test.
They also compared Inception-v3, Inception-slim, Inception-v4, and Inception-ResNet-v2;

## Slide 5: Literature Review
3
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm
Key Results
97% classification accuracy
98% F1-score
Improved performance on imbalanced dataset
Reduced redundant image features
Effective automated nanoparticle classification
Methodology
SEM images of Pd nanoparticles
Manual labeling into 5 morphology classes
Image preprocessing and filtering
Transfer learning with VGG-19
Grey Wolf Optimization for feature selection
Weighted SVM for final classification

## Slide 6: Objective
Target Classes (8)
Deep Learning Model for Classification
SEM Images of MEMS devices and components
The objective of this project is to develop an automated image classification system capable of recognizing different MEMS structures from SEM images using deep learning techniques.
Electrode | 92%
Cantilever | 4.3%
waveguide | 0.7%
… | 
Prediction
4
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 7: Dataset Characterization
03
Image preprocessing
Metadata removal and grayscale training
80/20 train-validation split (additional unlabeled images were used only for inference inspection)
02
Manual Annotation
01
Data Collection
4,158 SEM images from Kaggle
(NFFA-EUROPE - SEM Dataset)
2,800 images categorized into 8 classes
5
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 8: Model
Pretrained Features
Leverages knowledge from millions of images to learn general features (edges, textures, shapes).
well-established and widely validated deep learning architecture for image classification.
Better accuracy with limited data due to powerful feature representation.
uses residual connections, which allow the network to be much deeper while avoiding the vanishing gradient problem.
ResNet-50
Improved Performance
Reliable Baseline
Why Pre-trained ResNet-50 as baseline?
ResNet-50
Pretrained Weights/ Cropped SEM Images
8 classes with Accuracy of 92.97%
Final classification layer has been replaced and fine-tuned the model on MEMS dataset for 8 classes.
learning rate: 0.00003
Number of epochs: 20
batch size: 16
freeze-backbone-epochs: 3
6
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 9: Model
Target Classes (8)
precision: 0.97
recall: 1.0
f1-score: 0.99
support: 165
precision: 0.97
recall: 0.99
f1-score: 0.97
support: 94.0
precision: 0.87
recall: 1.0
f1-score: 0.93
support: 7.0
precision: 0.92
recall: 0.84
f1-score: 0.88
support: 132.0
precision: 0.86
recall: 0.90
f1-score: 0.88
support: 126.0
precision: 0.0
recall: 0.0
f1-score: 0.0
support: 1.0
precision: 1.0
recall: 0.25
f1-score: 0.4
support: 4.0
precision: 0.90
recall: 1.0
f1-score: 0.94
support: 26.0
ResNet-50
Pretrained Weights/ Cropped SEM Images
8 classes with Accuracy of 92.97%
Final classification layer has been replaced and fine-tuned the model on MEMS dataset for 8 classes.
learning rate: 0.00003
Number of epochs: 20
batch size: 16
freeze-backbone-epochs: 3
6
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 10: Model Development and Evaluation
Gray area (sample region) is cropped and used to train the baseline model.
OCS is applied to extract test from the white ribbon and save it as structured data in a CSV file.
Structured Metadata is used as additional features (metadata input) and combined with image features in the baseline model.
1. Cropped Image
2. OCR Extraction
3. Feed the Metadata Features to Model
4. Hyperparameter Changes
Experiment 1
Epoch : 30
Learning Rate: 1e-5
Freeze-backbone epoch: 3
Experiment 2
Epoch : 20
Learning Rate: 3e-5
Freeze-backbone epoch: 0
Training
Metadata
Grey Image Input
Output
Grey Image Input
Output
7
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 11: Model Development and Evaluation
Gray area (sample region) is cropped and used to train the baseline model.
OCS is applied to extract test from the white ribbon and save it as structured data in a CSV file.
Structured Metadata is used as additional features (metadata input) and combined with image features in the baseline model.
1. Cropped Image
2 OCR Extraction
3. Feed the Metadata Features to Model
4. Hyperparameter Changes
Experiment 1
Epoch : 30
Learning Rate: 1e-5
Freeze-backbone epoch: 3
Experiment 2
Epoch : 20
Learning Rate: 3e-5
Freeze-backbone epoch: 0
Training
Metadata
Grey Image Input
Output
Grey Image Input
Output
7
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 12: Model Development and Evaluation
Gray area (sample region) is cropped and used to train the baseline model.
OCS is applied to extract test from the white ribbon and save it as structured data in a CSV file.
Structured Metadata is used as additional features (metadata input) and combined with image features in the baseline model.
1. Cropped Image
2 OCR Extraction
3. Feed the Metadata Features to Model
4. Hyperparameter Changes
Experiment 1
Epoch : 30
Learning Rate: 1e-5
Freeze-backbone epoch: 3
Experiment 2
Epoch : 20
Learning Rate: 3e-5
Freeze-backbone epoch: 0
Training
Metadata
Grey Image Input
Output
Grey Image Input
Output
7
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 13: Model Development and Evaluation
Gray area (sample region) is cropped and used to train the baseline model.
OCS is applied to extract test from the white ribbon and save it as structured data in a CSV file.
Structured Metadata is used as additional features (metadata input) and combined with image features in the baseline model.
1. Cropped Image
2 OCR Extraction
3. Feed the Metadata Features to Model
4. Hyperparameter Changes
Experiment 1
Epoch : 30
Learning Rate: 1e-5
Freeze-backbone epoch: 3
Experiment 2
Epoch : 20
Learning Rate: 3e-5
Freeze-backbone epoch: 0
Training
Metadata
Grey Image Input
Output
Grey Image Input
Output
7
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 14: Model Development and Evaluation
Gray area (sample region) is cropped and used to train the baseline model.
OCS is applied to extract test from the white ribbon and save it as structured data in a CSV file.
Structured Metadata is used as additional features (metadata input) and combined with image features in the baseline model.
1. Cropped Image
2 OCR Extraction
3. Feed the Metadata Features to Model
4. Hyperparameter Changes
Experiment 1
Epoch : 30
Learning Rate: 1e-5
Freeze-backbone epoch: 3
Experiment 2
Epoch : 20
Learning Rate: 3e-5
Freeze-backbone epoch: 0
Training
Metadata
Grey Image Input
Output
Grey Image Input
Output
7
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 15: Results and Discussion
Learning rate
lower learning rate did not improve the model.
Metadata
improved early training performance and reached higher validation accuracy in the first few epochs.
Epoch
Increasing epochs alone is unlikely to improve performance.
Freeze backbone epoch
The pretrained ResNet-50 features were already suitable for SEM gray Image, so unfreezing the backbone from the start did not clearly improve performance.
8
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 16: Challenges and Errors
01
Manual image classification
manually sorting data into 8 categories was time-consuming and introduced the risk of human labeling mistakes, especially for visually similar classes such as close_up_line and Electrode.
Separating SEM image from microscope information
Each image contained a gray SEM region and a white microscope information ribbon. Using the full image could make the model learn from text or scale information instead of the actual structure.
02
Class imbalance
Some classes had many images, while others had very few, such as microfluidic, cantilever, and label. This could bias the model toward majority classes.
03
ML for business
Modeling challenge
More complex models did not automatically perform better. Adding OCR metadata and changing hyperparameters reduced or did not improve accuracy.
04
9
Classification of MEMS SEM Images using ResNet 50 - Negar Ziehm

## Slide 17
Thanks for your attention!
Questions are welcome,
Easy ones are appreciated 
MEMS